## Slide 1: 第五章 网络层: 控制平面
Slides are adapted from those of by J.F Kurose and K.W. Ross with copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: 第五章 网络层
本章目标:
弄懂网络控制平面背后的原理:
  传统的路由算法
  SDN 控制器
  互联网控制报文协议
  网络管理
及其在互联网中的实例化、实现
  OSPF, BGP, OpenFlow, ODL 及 ONOS 控制器, ICMP, SNMP
- 控制平面

## Slide 3: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 4: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 5: 网络层功能
转发: 将数据报从路由器的输入端转移到恰当的路由器输出端
构建网络控制平面的两种方法:
每路由器控制(传统)
逻辑集中控制(软件定义网络)
数据平面
控制平面
回顾: 两个网络层功能:
路由: 确定数据报从源到目标采用的路径
5.1 概述

## Slide 6: 每路由控制平面
路由
算法
数据
平面
控制
平面
5.1 概述
每个路由器中的路由算法模块互相在控制平面中交互以计算转发表
本地转发表
首部 输出
0100 3
0110 2
0111 2
1001 1

## Slide 7: 逻辑集中的控制平面
独立(通常是远程)控制器与路由器中的本地控制代理（CA）交互以计算转发表
5.1 概述
数据
平面
控制
平面
远程控制器
CA
CA
CA
CA
CA
1
2
0111
3
到达分组首部的值

## Slide 8: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 9: 路由协议
路由协议目标: 通过路由器网络确定从发送主机到接收主机的 "好" 路径(等价于路由)
路径: 分组从给定的源主机到给定的最终目标主机将穿过的路由器序列
"好": 最低 "开销", "最快", "最少拥塞"
路由选择: 一个 "前10" 网络挑战!
5.2 路由选择算法

## Slide 10: 网络的图抽象
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
图: G = (N,E)
N = 路由器集合 = { u, v, w, x, y, z }
E = 链路集合 ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
旁白: 图抽象在其它网络语境中亦很有用, 例如 P2P,
其时 N 是一组对等方而 E 则是一组 TCP 连接
5.2 路由选择算法

## Slide 11: 图抽象: 开销
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x') = 链路 (x,x') 的开销
例 c(w,z) = 5
开销可以总为 1, 或与带宽成反比, 或与拥塞相关连
路径 (x1, x2, x3,…, xp) 的开销 = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
关键问题: 在 u 与 z 之间最小开销的路径是什么?
路由算法: 找出最小开销路径的算法
5.2 路由选择算法

## Slide 12: 路由算法分类
Q: 全局或分散式信息?
全局:
所有路由器都具有完整的拓扑、链路开销信息
"链路状态" 算法
分散式:
路由器知道其物理上连接的邻居、到邻居的链路开销
迭代的计算过程及与邻居交换信息
"距离向量" 算法
Q: 静态或动态?
静态:
路由随时间变化缓慢
动态:
路由变化更快
  周期更新
  响应链路开销的变化
5.2 路由选择算法

## Slide 13: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 14: 链路状态路由算法
Dijkstra 算法
所有节点已知网络拓扑、链路开销
  通过 "链路状态广播" 完成
  所有节点具有相同的信息
计算从一个节点("源")到所有其它节点的最小开销路径
  为该节点提供转发表
迭代:经过 k次迭代, 知道 k 个目标的最小开销路径
记号:
c(x,y): 从节点 x 到 y 的链路开销; = ∞ 如果不是直接相邻
D(v): 从源到目标 v 的路径开销的当前值
p(v): 从源到 v 路径上的前一节点
N': 节点集，其最小开销路径已确知
5.2 路由选择算法
5.2.1 The Link-State (LS) Routing Algorithm
Notes: /ˈdɑɪkstɹə/

## Slide 15: Dijsktra 算法
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'
5.2 路由选择算法
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 16: Dijsktra 算法
5.2 路由选择算法
Dijkstra 最短路径算法
  G=(V,E)是一个带权有向图，V分成两组S和T，V=S U T。S为已求出最短路径的顶点集合。初始S中只有一个源点v，以后每求得一条最短路径 , 就将加入S中，直到S=V。从T中找出到v最短路径的点p依次加入S中。在加入的过程中，保持从v到S中各顶点的最短路径长度不大于从v到T的最短路径长度。每个顶点对应一个距离，S中的顶点的距离就是从v到此顶点的最短路径长度，T中顶点t的距离，是从v到t只包括S中的顶点为中间顶点的当前最短路径长度。流程：
  1) 初始时，S＝{v}，v的距离为0。T=V-{v}，若v与T中顶点u有边，则<u,v>正常有权值，若u不是v的邻接点，则<u,v>权值为∞
  2) 从T中选取一个距离v最小的顶点k加入S中(该距离就是v到k的最短路径长度)
  3) 以k为中间点，修改T中各顶点的距离；若从源点v到顶点u的距离（经过顶点k）比原来距离（不经过顶点k）短，则修改顶点u的距离值为v到k的距离加上k到u的距离(k到u的边的权)，修改后的距离值的顶点k的距离加上边上的权
  4) 重复2)和3)直到所有顶点都包含在S中
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 17: Dijsktra 算法
5.2 路由选择算法
Dijkstra 最短路径算法
  G=(V,E)是一个带权有向图，V分成两组S和T，V=S U T。S为已求出最短路径的顶点集合。初始S中只有一个源点v，以后每求得一条最短路径 , 就将加入S中，直到S=V。从T中找出到v最短路径的点p依次加入S中。在加入的过程中，保持从v到S中各顶点的最短路径长度不大于从v到T的最短路径长度。每个顶点对应一个距离，S中的顶点的距离就是从v到此顶点的最短路径长度，T中顶点t的距离，是从v到t只包括S中的顶点为中间顶点的当前最短路径长度。流程：
  1) 初始时，S＝{v}，v的距离为0。T=V-{v}，若v与T中顶点u有边，则<u,v>正常有权值，若u不是v的邻接点，则<u,v>权值为∞
  2) 从T中选取一个距离v最小的顶点k加入S中(该距离就是v到k的最短路径长度)
  3) 以k为中间点，修改T中各顶点的距离；若从源点v到顶点u的距离（经过顶点k）比原来距离（不经过顶点k）短，则修改顶点u的距离值为v到k的距离加上k到u的距离(k到u的边的权)，修改后的距离值的顶点k的距离加上边上的权
  4) 重复2)和3)直到所有顶点都包含在S中
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 18: Dijkstra 算法: 实例
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
uwxvyz
5.2 路由选择算法
注:
通过跟踪前导节点构造最短路径树
可能存在等距离情况 (从中任选即可)
5.2.1 The Link-State (LS) Routing Algorithm
Notes: predecessor node: 前导节点

## Slide 19: Dijkstra 算法: 另一实例
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
5.2 路由选择算法
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 20: Dijkstra 算法: 实例 (2)
u
y
x
w
v
z
生成源为 u 的最短路径树:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
目标
链路
生成节点 u 处的转发表:
5.2 路由选择算法
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 21: Dijkstra 算法, 讨论
算法复杂度: n 个节点
每次迭代: 需要检查所有节点, w  N
n (n + 1) / 2 次比较: O( n2 )
更高效的实现可能达到: O( n log n )
可能发生振荡:
例 支持链路的开销等于其当前承载的流量值:
A
D
C
B
1+e
e
0
e
1
1
0
0
最初
A
D
C
B
给定这些开销,
查找新路由…
产生新的开销
2+e
0
0
0
1+e
1
A
D
C
B
给定这些开销,
查找新路由…
产生新的开销
0
2+e
1+e
1
0
0
A
D
C
B
给定这些开销,
查找新路由…
产生新的开销
2+e
0
0
0
1+e
1
5.2 路由选择算法
1
5.2.1 The Link-State (LS) Routing Algorithm

## Slide 22: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 23: 距离向量算法
Bellman-Ford 方程 (动态规划)
设
dx( y ) := 从 x 到 y 的最小开销路径的开销
则
dx( y ) = minv {c(x,v) + dv( y ) }
到邻居 v 的开销
min 取值于所有 x 的邻居 v
从邻居 v 到目标 y 的开销
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 24: Bellman-Ford 实例
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
显然, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
取得最小值的节点是最短路径的下一跳而在转发表中被使用
由 B-F 方程:
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 25: 距离向量算法
Dx(y) = 从 x 到 y 的最小开销估算
  x 维护距离向量 Dx = [Dx(y): y є N ]
节点 x:
  知道到达每个邻居 v 的开销: c(x,v)
  维护其邻居的距离向量. 对每一邻居 v, x 维护 Dv = [Dv(y): y є N ]
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 26: 距离向量算法
关键思想:
每个节点不时地向邻居发送自己的距离向量估计值
当节点 x 收到其邻居的 DV 新估计值后, 它采用 B-F 方程来更新自己的 DV:
在非常少且自然的条件下, Dx(y) 的估计值收敛到真实的最小开销 dx(y)
Dx(y) ← minv{c(x,v) + Dv(y)} 对每个节点 y ∊ N
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 27: 距离向量算法
迭代、异步:
导致本地迭代的原因:
本地链路开销的改变
邻居的DV更新信息
分布式:
每个节点仅在其 DV 更改时通知邻居
  如有必要邻居会通告其邻居
每一节点:
等待 (本地链路开销改变或来自邻居的更改消息)
重新计算 估值
如果到任一目的地的 DV 发生改变, 通告 邻居
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 28
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 29
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 30: 距离向量: 链路开销改变
链路开销改变：
节点探测到本地链路开销的改变
更新路由信息, 重新计算距离向量
如果 DV 发生改变则通告邻居
"好消息传播快"
x
z
1
4
50
y
1
t0 : y 检测到链路开销改变, 更新其 DV, 通告邻居.
t1 : z 接收到来自 y 的更新, 更新其表, 计算到 x 新的最小开销, 将其 DV 发送给其邻居.
t2 : y 收到 z 的更新, 更新其距离表. y 的最小开销未改变, 于是 y 不发送消息给 z.
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 31: 距离向量: 链路开销改变
链路开销改变:
节点探测到本地链路开销的改变
坏消息传播慢 - "无穷计数" 问题!
算法稳定前经过44次迭代: 见课本
x
z
1
4
50
y
60
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm
算法继续进行!
X 到 Y
经过
X 到 Z
经过
X Z
4 6
X Y
50 5
时间轴
t0
X Z
60 6
X Y
50 5
t1
X Z
60 6
X Y
50 7
t2
X Z
60 8
X Y
50 7
t3
X Z
60 8
X Y
50 9
t4
c(X,Y) 改变
"无穷计算"

## Slide 32: 距离向量: 链路开销改变
x
z
1
4
50
y
60
反向下毒:
如果 Z 通过 Y 路由到 X:
  Z 通告 Y 它(Z) 到 X 的距离是无穷大 (从而 Y 不会通过 Z 路由到 X)
这一方法能彻底解决 "无穷计数" 问题吗?
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm
算法
终止
X 到 Y
经过
X 到 Z
经过
X Z
4 
X Y
50 5
时间
轴
t0
X Z
60 
X Y
50 5
t1
X Z
60 
X Y
50 61
t2
X Z
60 51
X Y
50 61
t3
X Z
60 51
X Y
50 
t4
c(X,Y) 改变
当含有多于3个邻居的环路时就会失败
"无穷计算"

## Slide 33: 距离向量: 链路开销改变
5.2 路由选择算法
https://en.wikipedia.org/wiki/Distance-vector_routing_protocol#Count-to-infinity_problem
无穷计数问题解决方案
设置无穷大 = “一个小整数” (例如 16). 当计数 = 16 时停止.
水平分割: 若 C 从 B 获取最低开销路径，则它不向 B 通告开销
反向下毒: C 通告无穷大给 B
Bellman-Ford 算法有许多问题(和修补方法)
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 34: 距离向量: 链路开销改变
链路开销改变:
节点检测到本地链路开销变化
坏消息传得慢 - "无穷计算" 问题!
算法稳定前44次迭代: 参见课本
x
z
1
4
50
y
60
反向下毒:
如果 Z 通过 Y 路由到达 X :
  Z 告知 Y 其 (Z 的) 到 X 的距离是无穷大 (使得 Y不会通过 Z 路由到 X)
这能彻底解决无穷计数问题吗?
5.2 路由选择算法
导致无穷计算问题的原因是把从对方获知的，但在对方已不再有效的信息当成有效信息再传送给对方，使对方当成有效信息使用。
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 35: LS 与 DV 算法比较
消息复杂度
LS: n 个节点, E 条链路, O(nE) 消息送出
DV: 只在邻居间交换消息
  收敛时间变化
收敛速度
LS: O(n2) 算法需要 O(nE) 条消息
  可能有振荡
DV: 收敛时间变化
  可能循环路由
  无穷计算问题
健壮性: 如果路由器产生故障会发生什么?
LS:
  节点通告不正确的链路开销
  每个节点只计算自己的路由表
DV:
  DV 节点通告不正确的路径开销
  每一节点的表被其它节点采用
    错误通过网络被传播
5.2 路由选择算法
5.2.2 The Distance-Vector (DV) Routing Algorithm

## Slide 36: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 37: 使路由算法可扩展
规模: 有数十亿目的地:
无法将所有目的地都存储在路由表中!
路由表的交换将忙死链路!
管理自治
互联网 = 网络的网络
每个网管都希望控制路由在各自的网络内进行
我们迄今为止的路由算法学习 – 理想化
所有路由器都相同
网络 "扁平"
… 实践中不是如此
5.3 OSPF

## Slide 38: 可扩展路由的互联网实现
将路由器聚集到称为"自治系统" (AS，亦称 "域")的区域中
域间路由
在 AS 之间进行路由
网关执行域间路由(也进行域内路由)
域内路由
在同一 AS ("网络")内的主机、路由器之间路由
AS中的所有路由器必须运行相同的域内协议
不同AS中的路由器可以运行不同的域内路由协议
网关路由器: 在其自身的 AS 的 "边缘", 有到其它 AS 的路由器的链路
5.3 OSPF

## Slide 39: 互联的 AS
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
域内
路由
算法
域间
路由
算法
转发表
3c
转发表既被域内也被域间路由算法进行配置
  域内路由确定目的在域内的路由条目
  域间及域内确定外部目标的路由条目
5.3 OSPF

## Slide 40: 域间任务
假设AS1中的路由器接收到发往AS1之外的数据报:
  路由器应该把数据报转发给网关路由器，但选哪一个呢?
AS1 必须:
知道哪些目标通过 AS2 可达, 哪些通过 AS3
将此可达信息传播到 AS1 中的所有路由器
域间路由选择的任务!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
5.3 OSPF

## Slide 41: 域内路由
也称为内部网关协议(IGP, Interior Gateway Protocol)
最常见的域内路由协议:
  RIP: Routing Information Protocol(路由信息协议)
  OSPF: Open Shortest Path First (IS-IS 协议与 OSPF 基本相同)
  IGRP: 内部网关路由协议 (Cisco 私有数十年, 直到2016)
5.3 OSPF

## Slide 42: OSPF (开放最短路径优先)
"开放": 公开可用
采用链路状态算法
  链路状态分组传播
  每一节点的拓扑图
  采用 Dijkstra 算法路由计算
路由器洪泛 OSPF 链路状态通告到整个域内的所有其它路由器
  直接在 IP 上通过 OSPF 消息携带 (而不是 TCP 或 UDP)
  链路状态: 对每个相连的链路
IS-IS 路由协议: 与 OSPF 近乎相同
5.3 OSPF
Intermediate System to Intermediate System
https://en.wikipedia.org/wiki/IS-IS
Open Shortest Path First
Notes: IS-IS: Layer 2 protocol
OSPF: Layer 3 protocol

## Slide 43: OSPF "高级" 特点
安全: 对所有 OSPF 消息进行鉴证 (防范恶意入侵)
容许多个相同开销路径 (而 RIP 中只有一个路径)
对每个链路, 对不同服务条款(TOS, Terms of Service )提供多开销测度(例如，卫星链路对尽力而为的服务设置成低开销；而对实时服务设置为高)
集成单播和多播支持:
  多播 OSPF (MOSPF) 使用与OSPF相同的拓扑数据库
在大型域中采用 分层 OSPF
5.3 OSPF
Notes: 服务条款

## Slide 44: 分层 OSPF
边界路由器
主干路由器
区域 1
区域 2
区域 3
主干
区域
边界
路由器
内部
路由器
5.3 OSPF

## Slide 45: 分层 OSPF
两级分层: 局域, 主干
  仅在区域中通告链路状态
  每个节点都有详细的区域拓扑; 只知道到其他区域中网络的方向 (最短路径)
区域边界路由器: "归纳" 到本区域中网络的距离, 通告给其它的区域边界路由器
主干路由器: 运行限于主干的 OSPF 路由
边界路由器: 连接到其它 AS.
5.3 OSPF

## Slide 46: Homework
本章选做3道，一周内提交
第5章 网络层 - 控制平面

## Slide 47: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 48: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain 路由协议
  "glue that holds the Internet together"
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine "good" routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: "I am here"
5.4 BGP

## Slide 49: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protools
5.4 BGP

## Slide 50: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers ("peers") exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a "path vector" protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X
5.4 BGP

## Slide 51: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = "route"
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other neighboring ASes
5.4 BGP

## Slide 52: BGP path advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
5.4 BGP

## Slide 53: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP
5.4 BGP

## Slide 54: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection
5.4 BGP

## Slide 55: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: "path to X goes through 1c"
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d
5.4 BGP

## Slide 56: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: "path to X goes through 1c"
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2
5.4 BGP

## Slide 57: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
5.4 BGP

## Slide 58: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don't worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263
5.4 BGP

## Slide 59: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no "revenue" for routing CBAw, since none of C, A, w are B's customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
5.4 BGP

## Slide 60: BGP: achieving policy via advertisements
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)
5.4 BGP

## Slide 61: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance
5.4 BGP

## Slide 62: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 63
Software defined networking (SDN)
Internet 网络层: historically has been implemented via distributed, 每路由 approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different "middleboxes" for different 网络层 functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network 控制平面
5.5 The SDN 控制平面

## Slide 64
Recall: 每路由 控制平面
Routing
算法
Individual 路由算法 components in each and every router interact with each other in 控制平面 to compute forwarding tables
data
plane
control
plane
5.5 The SDN 控制平面

## Slide 65
data
plane
control
plane
Recall: 逻辑集中的 控制平面
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA
5.5 The SDN 控制平面

## Slide 66
Software defined networking (SDN)
Why a 逻辑集中的 控制平面?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows "programming" routers
  centralized "programming" easier: compute tables centrally and distribute
  distributed "programming: more difficult: compute tables as result of distributed 算法 (protocol) implemented in each and every router
open (non-proprietary) implementation of 控制平面
5.5 The SDN 控制平面

## Slide 67: Analogy: mainframe to PC evolution*
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
5.5 The SDN 控制平面

## Slide 68: Traffic engineering: difficult traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic 路由算法 computes routes accordingly (or need a new 路由算法)!
Link weights are only control "knobs": wrong!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
5.5 The SDN 控制平面
Notes: Note: implicit assumption here: destination based forwarding

## Slide 69: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can't do it (or need a new 路由算法)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
5.5 The SDN 控制平面
Notes: Note: implicit assumption here: destination based forwarding

## Slide 70: Traffic engineering: difficult
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route orange and red traffic differently?
A: can't do it (with destination based forwarding, and LS, DV routing)
5.5 The SDN 控制平面
Notes: Note: implicit assumption here: destination based forwarding

## Slide 71
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized" flow-based" forwarding (e.g., OpenFlow)
2. control, 数据平面 separation
3. 控制平面 functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance
5.5 The SDN 控制平面

## Slide 72
SDN perspective: 数据平面 switches
数据平面 switches
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN 控制平面

## Slide 73
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications "above" via northbound API
interacts with network switches "below" via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN 控制平面

## Slide 74
SDN perspective: control applications
network-control apps:
"brains" of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
5.5 The SDN 控制平面

## Slide 75
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API
5.5 The SDN 控制平面

## Slide 76: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)
OpenFlow Controller
5.5 The SDN 控制平面
port # 6653

## Slide 77: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller
5.5 The SDN 控制平面

## Slide 78: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don't "program" switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller
5.5 The SDN 控制平面

## Slide 79
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
SDN: control/数据平面 interaction example
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra's 路由算法 application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra's 路由算法 access network graph info, 链路状态 info in controller, computes new routes
4
5.5 The SDN 控制平面

## Slide 80
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra's link-state
Routing
s1
s2
s3
s4
SDN: control/数据平面 interaction example
链路状态 routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6
5.5 The SDN 控制平面

## Slide 81
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
OpenDaylight (ODL) controller
ODL Lithium controller
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services
5.5 The SDN 控制平面
https://wiki.opendaylight.org/view/OpenDaylight_Controller:REST_Reference_and_Authentication
Neon
Notes: Neon: Version 10

## Slide 82
Network
control apps
…
REST API
ONOS
distributed core
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
ONOS controller
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling
5.5 The SDN 控制平面

## Slide 83
SDN: selected challenges
hardening 控制平面: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for 控制平面
  dependability, security: "baked in" from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling
5.5 The SDN 控制平面

## Slide 84: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 85: ICMP: Internet Control Message Protocol
由主机和路由器用于通信交换网络级信息
  错误报告: 不可达的主机、网络、端口、协议
  回显请求/应答 (由ping使用)
IP"之上"的网络层:
  ICMP消息由IP数据报承载
ICMP 消息: 类型、编码加上导致错误的IP数据报的前8个字节
类型 编码 描述
0 0 回显应答(ping)
3 0 目标网络不可达
3 1 目标主机不可达
3 2 目标协议不可达
3 3 目标端口不可达
3 6 目标网络未知
3 7 目标主机未知
4 0 源抑制(拥塞控制 – 未使用)
8 0 回显请求(ping)
9 0 路由器通告
10 0 路由器发现
11 0 TTL 超期
12 0 IP 首部损坏
5.6 ICMP
Notes: source quench: 源抑制

## Slide 86: Traceroute 与 ICMP
源向目标发送一系列UDP报文段
  第一组具有 TTL =1
  第二组具有 TTL=2, 依次类推
  不可达端口号 (例如 80)
当第 n 组数据报到达第 n 个路由器:
  路由器丢弃数据报并发给源端 ICMP 消息 (类型 11, 编码 0)
  ICMP 消息含有路由器名称和IP地址
当 ICMP 消息到达时, 源端记录 RTT
停止条件:
UDP 报文段最终到达目的主机
目标返回 ICMP "端口不可达" 消息 (类型 3, 编码 3)
源端停止
3 probes
3 probes
3 probes
5.6 ICMP
80 是 HTTP 端口, 基于 TCP,
对 UDP 来说是 unlikely

## Slide 87: 第五章 网络层 - 控制平面
5.5 SDN 控制平面
5.6 ICMP: 互联网控制报文协议
5.7 网络管理与 SNMP
5.1 概述
5.2 路由选择算法
  链路状态
  距离向量
5.3 互联网自治系统内的路由算法: OSPF
5.4 ISP 之间的路由: BGP
第5章 网络层 - 控制平面
Notes: SDN: software defined network

## Slide 88: What is network management?
自治系统 (aka "network"): 1000s of interacting hardware/software components
other complex systems requiring monitoring, control:
  jet airplane
  nuclear power plant
  others?
"Network management includes the deployment, integration
and coordination of the hardware, software, and human
elements to monitor, test, poll, configure, analyze, evaluate,
and control the network and element resources to meet the
real-time, operational performance, and Quality of Service
requirements at a reasonable cost."
5.7 SNMP
Notes: poll: 轮询、挂起到队列

## Slide 89: Infrastructure for network management
managed device
managed device
managed device
managed device
definitions:
managed devices contain managed objects whose data is gathered into a Management Information Base (MIB)
managing
entity
data
managing entity
agent
data
agent
data
network
management
protocol
managed device
agent
data
agent
data
agent
data
5.7 SNMP

## Slide 90: SNMP protocol
Two ways to convey MIB info, commands:
agent
data
managed device
managing
entity
agent
data
managed device
managing
entity
trap msg
request
request/response mode
trap mode
response
5.7 SNMP
Notes: trap message: 陷阱报文，例如链路接口的启动与关闭时发送非请求报文

## Slide 91: SNMP protocol: message types
GetRequest
GetNextRequest
GetBulkRequest
manager-to-agent: "get me data"
(data instance, next data in list, block of data)
Message type
Function
InformRequest
manager-to-manager: here's MIB value
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to
Request
Trap
Agent-to-manager: inform manager
of exceptional event
5.7 SNMP
SNMP operates in the application layer
SNMP messages are transported via UDP
protocol data unit — PDU

## Slide 92: SNMP protocol: message formats
….
PDU
type
(0-3)
Request
ID
Error
Status
(0-5)
Error
Index
Name
Value
Name
Value
….
PDU
type
4
Enterprise
Agent
Addr
Trap
Type
(0-7)
Specific
code
Time
stamp
Name
Value
Get/set header
Variables to get/set
Trap header
Trap info
SNMP PDU
More on network management: see earlier editions of text!
5.7 SNMP
PDU format
Notes: PDU: Protocol Data Unit

## Slide 93
第五章 summary
we've learned a lot!
approaches to network 控制平面
  每路由 control (traditional)
  逻辑集中的 control (software defined networking)
traditional 路由算法
  implementation in Internet: OSPF, BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
network management
next stop: link layer!
第5章 网络层 - 控制平面

## Slide 94
TELNET
HTTP
FTP
SMTP
DNS
RIP
SNMP
DHCP
TCP
UDP
IP
ICMP
OSPF
ARP
RARP
application layer
transport
layer
network
layer
The Internet Hourglass
link
layer
ethernet
802.11
SONET
ATM
第5章 网络层 - 控制平面

## Slide 95: Homework
本章选做3道，一周内提交
第5章 网络层 - 控制平面